## Slide 1: ODW Data Dictionary Package
Jim Philbin

## Slide 2: Dictionary Package
The dictionary package is the home of DICOM constant classes such as:
VM– value multiplicity
VR – value representation
Tag – a class containing all the information (including VM, VR, Etype,…) about DICOM Data Element Definitions, aka semantic identifiers
Macro – DICOM macros (future)
Module – DICOM modules (future)
IOD – DICOM IODs (future)

## Slide 3: Requirements
The Toolkit and applications should work with
  All major browsers,
  Android devices,
  IOS devices
  Chromium?
Applications should load within 1 second.
A study with 250 images should complete profile analysis within 3 seconds.
Applications should support Liquid Design

## Slide 4: Tag Class The Tag class defines a semantic concept
PS3.6 contains the Data Element Definitions. Each definition corresponds to a semantic concept related to medical imaging. This is the heart of DICOM. The Tag defines :
Keyword
      A unique keyword associated with the concept. The keyword should contain only alphanumeric characters and underscore.
Code
  A numeric code (traditionally called a Tag) that uniquely defines this concept.
  Note: Code is call “tag” in the standard.
Name
  A short English descriptive phrase for the concept.
VM
  The minimum, maximum, and with of the array of values associated with this concept
VR
  The data type of the values of this concept
Type
  The Element Type (1, 1c, 2, 2c, 3) of this concept. This describes the requirement on the presence of the concept in a particular IOD. Many of the Semantic concepts always have the same type, which is why it is included in Tag.
IsRetired
  A Boolean value specifying whether this concept has been retired.
IsPublic, IsPrivate…
  Predicate describing whether the Tag is Public, Private Creator, Private Data, etc.
The Tag also define many useful Getters and Methods:
Group, Elt, dcm, hex…
Min, max, width
vrIndex, sizeInBytes, isShort…
checkValues, checkValue
getErrors

## Slide 5: VM A constant class implementing DICOM Value Multiplicities
  minLength,
  maxLength,
  Width
  checkLength

## Slide 6: VR A constant class implementing DICOM Value Representations
VR
  index
  sizeInBytes
  isShort

## Slide 7: Conditions
Present The Element shall be present
Not Present The Element shall not be present
If Present(conditions) If the Element is present, then the conditions shall be true

## Slide 8: Validators
Range:
  [x, y] inclusive
  (x, y) exclusive
  [x, y) includes x, but not y
  (x, y] includes y, but not x